`

`

Paper for CosRay/RET

31 July 2003

by

Elisabeth B. Langford

Project supported by a grant from

The National Science Foundation

Research Experience for Teachers

Science Department

Springfield Southeast High School

2350 East Ash Street

Springfield, IL 62703

Table of Contents

| Overview | 1 |
| --- | --- |
| Introduction | 1 |
| Specific Procedures | 2 |
| Problems Encountered | 4 |
| Conclusions | 5 |
| Future Plans | 7 |
| Appendix A Figures | 9 |
| Appendix B Constants & Basic Concepts | 15 |
| Appendix C Calculations | 16 |
| Appendix D Data | 18 |
| Appendix E Statistical Analysis | 25 |
| Appendix F Graphs | 32 |
| lstack | 32-33 |
| Single count by counter vs. voltage | 34 |
| Typical qvt graphs | 35 |
| Overlap graph | 38 |
| Appendix G Glossary | 9 |
| Appendix H Citations | 42 |

Overview:

This project was performed from 23 June through 18 July 2003.  The purpose was to study cosmic rays and their detection, in order to involve high school students enrolled in Science of the Physical World, members of the Science Club, and other interested students in cosmic ray research.

Introduction:

Cosmic rays are high-energy [109 eV [Gev] to over 1020 eV] charged particles with half-lives of 106 seconds or longer.  They travel at relativistic speeds and originate in outer space in stars and other events such as supernovas.  They may be protons, a few electrons, and/or the nuclei of helium, carbon, or oxygen.  These primary particles interact with other particles either in outer space or in our atmosphere.  These interactions produce a cascade of secondary particles of pions, mesons, muons, neutrinos, electrons, photons, and the nuclei of lithium, beryllium, and boron, as a secondary shower.  These in turn may interact with other particles producing tertiary showers.  Muons are the most numerous particles that reach the surface of the Earth, with a mean energy level at sea level of ( 4GeV.  Other particles that may reach Earth’s surface are photons, electrons, positrons, and neutrinos.

When a cosmic ray, such as a proton, collides with a nucleus in our atmosphere, some of the energy of the proton is transferred to the other nucleus.  This interaction can cause a variety of high-energy particles to be produced.  These particles are classified as either hard [particles that will penetrate large amount of material, these are mostly muons] and soft [particles that will be attenuated by material these are mostly electrons].  The particles in the soft component of a cosmic ray have lower energies and interact more readily with other nucleons.

A general overview of the process by which these cosmic rays were studied is that when a particle entered the scintillator, the particle excited a scintillator molecule; in losing the energy gained from the particle, the molecule emitted a photon that bounced to the end of the scintillator; the photon then passed through the light guide to the photomultiplier.  Approximately 2 to 3 %  of the photons produced reached the photomultiplier.  When the photon reached the first dynode of the photomultiplier, an electron was emitted by the dynode because of the photoelectric effect.  When the electron struck the second dynode, the second dynode gave off more electrons, this process continued down the line of dynodes.  At the end of the photomultiplier, the electrons became a signal that was sent to the Analog Digital Converter [ADC] and then to the computer.

Scintillator counters are made from aromatic plastic compounds doped with fluors that are excited by the muons.  When a muon strikes a molecule in the scintillator, the muon imparts some of its energy to the molecule.  The addition of this energy, excites the

molecule.  The molecule in returning to a lower energy state, releases some of the energy in the form of a photon.  A “typical particle yields about 1 photon per 100 eV of energy deposit.”.  If the photons in the scintillator are emitted above the critical angle, they will remain in the counter, bouncing back and forth.  Some of these photons will reach the end of the scintillator where it is attached to a light guide.  This light guide funnels the photons to the photomultiplier.

When a photon strikes the first photo cathode in the photomultiplier, an electron is released due to the photoelectron effect.  This electron interacts with the second dynode, a metal plate, producing more electrons.  The final number of electrons produced by one electron emitted from the photo cathode is approximately 2n, where n is the number of dynodes [Thomas].

The signal from the anode [negative terminal, where the electrons are collected] of the photomultiplier is sent to the Analog Digital Converter, ADC, where the signal is digitized then sent to the computer.  The signal from the dynode, positive terminal with respect to the ground since more electrons leave than enter, goes to the discriminator.  The discriminator output is sent to the Coincidence and the Time Digital Converter, TDC.  The TDC is where the time signal is digitized, and its output is then sent to the computer.  The Coincidence requires a signal from a combination of one to four counters, e.g. the requirement could be that both counters 1 and 6 send a signal to the Coincidence within the same time period.  The ADC will send a signal to the computer if the Coincidence condition is satisfied.  The output of the Coincidence is then sent to the qvt terminal, the TDC start, and the ADC gate.

If two scintillators placed directly above each other, a cosmic ray would deposit energy in both scintillators at nearly the same time.  [Note: the time it takes a photon to travel thru two one-half centimeter thick counters is approximately 0.5 nanoseconds].  The signal generated by a photon is counted only if the two signals arrive at the timing gate at the same time.  Of course, the joint signals arise from one or more charged particles passing through the counters, arising from a common “event” and therefore in close time coincidence.  However, other mechanisms such as accidental overlap must still be considered.

##### Specific Procedures:

The counters, light guides and photomultipliers were wrapped in black plastic to exclude any outside sources of light.

The cable lengths are not measured in centimeters or meters, but in nanoseconds.  The electrical signals travel down the cables as waves.  The index of refraction for the cable is 1.6.  Using the equation v = c/n where v is the velocity in the medium, c is the speed of light, c and n is the index of refraction, the time for the signal to travel 18.75 centimeter is 1 nanosecond.

A pulse generator and an oscilloscope are used to measure the cables.  The signal from the pulse generator and the cable are connected by a T connector to the same channel of the oscilloscope.  The signal from the pulse generator is divided between the oscilloscope and the cable being measured.  The signal sent to the cable traveled the length of the cable, and then was reflected back to the oscilloscope.  The wave in a shielded cable acts like a wave on a string tied at one end and is reflected back in the opposite direction, inverted, while an open cable reflects the wave in the same direction, erect.  An open cable was used.  If the free end of the cable was shorted by using a paper clip, the signal was inverted.  In some cases, to be sure of the measurement, the two methods were compared.

The x-axis of the grid on the oscilloscope screen is time.  The units of this scale can be adjusted to be from 2 to 50 nanoseconds.  The length of the cable is the difference in time from the first signal from the pulse generator, to the second signal, reflected, divided by two [The reflected signal traveled the length of the cable twice].  With very short cables, having signal time of one to about three nanoseconds, it is often easier to measure the length of the cable with a tape measure.  With longer cables, the oscilloscope provides a faster and more accurate measurement.

Originally there were ten counters: two small ones, S1 and S2 made by David E Kraus, Kari van Brunt, and Debbie Gremmelsbacher; two made by Lenka Raska, LA and LB; and six large counters L1 – L6.  S1 and S2 were modified to be used as portable counters for schools [Gremmelsbacher], leaving eight for these investigations.

To analyze a counter using the qvt [charge, voltage, and time] portion of the dtake electronic module and software, three measurements had to be taken:

- The pedestal energy peak, this is the constant “trickle” of charge which the ADC always adds to each channel or bin as a calibration.  It is used as the base line to which other measurement must be referred.

- One photoelectron [PE] energy peak.

- The cosmic ray [CR] peak.

- A histogram was created by the qvt program with the x–axis being the channel or bin numbers.  Each bin was equal to 0.25 x 10-12 Coulombs of charge.

Each of the remaining counters [eight counters: LA; LB; and L1 - L6] was individually analyzed.  Counters, L1 – L6, were stacked so that their scintillators were directly above each other.  Counters LA and LB were moveable.

The first dtake option used the qvt software to study a counter; its anode cable was inserted into the q channel on the qvt module.  The dynode went to discriminator using a 20 mV threshold.  Usually the pedestal data were taken first.  This involved triggering on another counter, and taking a very short run, one to five seconds.  The information was displayed as a histogram on the computer screen.  Secondly, the PE was found.  There are two methods to find the PE.  The first used the external trigger on the qvt module and triggering on the counter being studied through the Discriminator and Coincidence circuit.  The second method used the internal trigger on the qvt and all triggers off on the Coincidence circuit.  To find the CR, the counter being studied and one or more of the other counter triggers were in the on position, i.e. elements of the coincidence trigger.  This method took longer, 5 –30 minutes to collect enough data.

The pedestal and the PE peak were frequently close to each other.  To gain better separation, the determinations of the pedestal and PE peak were run using a higher voltage.  A lower voltage was used for the CR peak, because it was frequently chopped off on the very right hand side of the scale.  The time used to measure the Pedestal and PE peak was small since only singles were measured, while a longer period was needed to collect enough cosmic rays.  The pedestal was quite sharp; this PE peak was well defined, but not sharp, and the CR curve was broader.

Attenuators were added to the ADC signal to decrease the signal, making it in the range of 500 bins for the “CR” signal.  It was decided that the best voltages available were: 2000 V for counters LA, L2, L4, and L6; 1900 V for L1, L3, and L5; and 1800 for LB.  The expected CR rate and PE peak were calculated for 2000 V.  The actual voltages used were determined from the expected PE peak and expected CR peak.

The second option for the dtake software was to analyze all of the counters, event by event, during one run rather than studying them individually.  Counter 3 was connected to the ADC, but not to the TDC.  All the other counters were had both ADC and TDC information.  Counters LA, L1, and L6 were put into the coincidence, Runs were taken triggered on LA, L1, L6 and LB, L1, and L6.  Both of these runs had no attenuation.

Several problems were encountered, i.e. one of them being that it was difficult to distinguish between the pedestal and PE peak.  Another was that for some of the counters the PE or CR curve was chopped.  This might have been due to an improper setting in the software.

Problems Encountered:

While studying the overlap and coincidence rates between counters LB and L1, the singles rate for LB was very high.  On 25 June, the singles rate for B was taken in a variety of positions rotating it perpendicular to L1 and rotating it so that each large side faced the window.  It was discovered that LB had a light leak.  This was resolved by taping the outer black plastic wrapping more thoroughly.  Later, while studying all of the counters during one run, an additional light leak was found in L5 [Godwin].

On 9 July counter L2 was giving problems.  It was discovered that the signal, going to the discriminator, was missing an inverter.  It is unknown when the inverter was removed, making earlier results uncertain.  The inverter was inserted in the anode circuitry eliminating the problem.

Some of the early low voltage results might have had the lower end of the pedestal truncated, making the PE – pedestals too high.  [JT]

The runs taken on the 23rd and 24th of June were not considered as reliable because of the lack of the familiarity of the equipment.

a few inconsistencies were noted.  When L1 was tested at 1900 Volts, the three results taken on 7 July are inconsistent with the rest of the data at 1900 V.  The reason for the inconsistencies is inconclusive.  L1 results were better at 1900 V than 2000 V where there was a ten-fold difference in one of the three readings.  L2 was tested only twice and at 2000 V, however the results are in good agreement.  L4 also showed consistent results at 2000 V.  L5 was tested once at 1800 V and once at 1900 V.  More testing is needed for L2, L3, L4, and L5 before any definite conclusions can be made.

Conclusions:

The thrust of the investigation was to verify the performance of the eight counters in order that they can be used for further investigations of cosmic rays.  S1 and S2 were excluded.  When making the ADC plots, L3 was not used since there were only seven working inputs on the TDC.  It was not possible to connect eight counters to the TDC; it was decided to not study counter L3.

Counters LB and L1 were studied using various overlapping distances.  The coincidence rates are linear.  This agrees with the results obtained during the summer of 2002 by Lenka Raska.  The first run was done at 2100 V for both counters and an overlap of 45 cm, which was complete overlap of LB on L1.  The singles count rates and the coincidence count rates were both very large.  The subsequent runs were done at 1800 V.  As can be seen from Table 4 in Appendix D when the accidental rate was subtracted from the coincidence rate the coincidence rate was slightly larger than the coincidence rate with an over lap of 45 cm.  Also

The counters were tested at various voltages.  Some of the voltages were determined to be too low to give adequate counts.  When the data were organized by counter, voltage, and count, the single counts versus voltage show the dramatic effect a photomultiplier began to functions as a multiplier.  This can be seen in the statistical analysis of the singles counts, and the graph Singles Counts by Counter Versus Voltage by Date”.  Both of these show an exponential relationship of the counts to the voltage.  The correlation found in the statistical analysis showed relatively high correlation.  The adjusted R square for LA was 0.89; for B was 0.85; for L1was 0.88; and for L6 was 0.88.  This analysis was not done for L2, L4, or L5 because there was insufficient number of observations.

The pedestal, PE, and CR peaks for various combinations of counters are shown in Appendix D Table 3.  There is variation in the PE and CR’s depending upon which counters were selected.  The number of counts depends upon where the energy is deposited.  The farther away from the photomultiplier the energy is deposited, the lower the count rate.  When the energy is deposited closer to the   photomultiplier the count rate increases.  This affects the expected number for both the  PE and CR  peaks. In Appendix F, the first two graphs are the ADC graphs.  The dark vertical lines were added to the graphs to indicate where the PE or CE is expected.  When there are two dark vertical lines, it shows the range of expected values.  The lstack graphs were made using L1, L2, L4, L5, and L6.  The expected values would be for energy deposited in the middle of the counters, Table 4 contains information for both the middle and the extremes, near and far from the photomultiplier.

The voltages were determined by the pulse heights, so that the cosmic ray signal would be about in the middle of the ADC range (to the extent possible, since there was not a full free range of selection).  The voltages selected were:

| Counter | Selection | Voltage |
| --- | --- | --- |
| LA | HV | 2000 V |
| LB | -200 V | 1800 V |
| L1 | -100 V | 1900 V |
| L2 | HV | 2000 V |
| L3 | -100 V | 1900 V |
| L4 | HV | 2000 V |
| L5 | -100 | 1900 V |
| L6 | HV | 2000 V |

Once the results from the qvt program were known, the dtake program was used.  This program allowed for as many as seven of the eight counters to be in coincidence during one run.

In collaboration with Mark Godwin, several runs were taken using the dtake program.  The counters were arranged so that the photomultipliers of L1, L3, and L5 were at one end of the stack and the photomultipliers of L2, L4, and L6 were at the other end of the stack.  When the ADC plots, obtained by using the dtake software from a run of counters L1, L3, and L5 were combined with the same run of L2, L3, and L4, two distinct groupings were noticed.  Photons produced closer in the end of the scintillator closest to the photomultiplier tube had a greater chance of reaching the photomultiplier, therefore being counted than did ones produced at the end of the scintillator farthest from the photomultiplier.  Continued study of counter L1 gave PE/CR ratios of 14.8, 11.3, and 25.5, when triggered on LA, L1, and L6.  LA was placed in the middle of the stack of counters.  LA gave a PE/CR ratio of 120 when triggering on LA, L1, and L6.  [Godwin]

The lstack graphs, show the results from two runs using L1, L2, L3, L4, L5, and L6.  These runs are discriminated by the use of dotted and solid lines.  The graphs showing data from the odd numbered stack are shown in solid lines and the even numbered stack are shown in dotted lines.  The variation between the two plots is because the photons closer to the photomultiplier have a greater chance of arriving at the photomultiplier than do the photons produced at the far end of a scintillator.  The photomultipliers of the odd numbered scintillators are at the opposite end from the photomultipliers of the even numbered scintillators.

This phenomenon is clearly shown in the graphs on the ADC Plots.  These are made by taking two runs under the same conditions, and then transferring the run data to Kaon, and using Physics Analysis Workstation [PAW] to overlay the two plots and analyze them.  The results of the ADC plots compared with the expected PE and CR are comparable.  The dark lines on the two graphs are where the expected rates would be.  As the ADC plots show, it makes a difference where in the scintillator the energy is deposited.  When energy is deposited closer to the photomultiplier tube, the likely hood of the photon reaching the PMT is greater than when it is deposited farther away from the PMT.

Since there is agreement of the ADC plots and the qvt data, the counters may be used for further studies of cosmic rays.

Future Plans:

I would like to engage students in learning about and participating in cosmic ray research as an after school activity.  I also would like to encourage another teacher, Jason Potter,  to help in recruiting and working with the students.  My first contacts will be through the Southeast Science Club, advised by Wanda Britt.  I will encourage my Science of the Physical World students to participate, by allowing them to substitute participation in the research for their projects due each quarter.  I would also like to extend the participation to the students of Jennifer Thomas, who teaches in a nearby district.

The plan is to give the students background information on cosmic rays such as:

- Background information about cosmic rays:

- Primary Cosmic Rays - what are they?

- Where do they originate?

- How do Primary Cosmic Rays interact?

- What particles are formed that form the secondary showers?

- What are the components of our detection equipment, i.e. counters?

  - Scintillator

  - Light guide (complete internal reflection) General discussion for those who are not familiar with trigonometry.  Use of Snell’s Law for those who have the math background.

  - Photo multiplier

- What is the photoelectric effect?

- What does a diode do?

- What particles from the secondary showers are we able to detect using scintillation detectors?

- How does our equipment work?

I would like to familiarize themselves with oscilloscopes using a stimulation model found on the Web.  With an actual oscilloscope, this would allow them to measure the length of the cables in nanoseconds.  Then we would begin actual experimentation.  If I can find a supply of dry ice, I would like to begin with the use of cloud chambers, first using known sources of radiation, and then to discover if we could find tracks of unknown origin.

The next step would be having them use the counters.  Finding single counter rates for both scintillators individually and then having them find the coincidences rates.  We have a courtyard, which would give easy access to electrical power for outside observations.  This would allow us to look at secondary cosmic ray showers and the delta rays produced by the cosmic rays traveling through the roofing materials.  We also could compare rates on the first floor with the rates on the second floor.

Another possibility is to have the students assemble and test their own counters.  If the equipment became available, it would be interesting to have them work with the dtake program, especially the qvt program and evaluate the scintillators that they made.

The final goal is to become part of a larger network, connected to a common computer in order to study the very high [1020eV] cosmic rays.  This would also require them to become familiar with the programs used with the Geo Positioning Satellite.

Appendix A

Figures

http://www.ngdc.noaa.gov/stp/SOLAR/COSMIC_RAYS/cosmic.html

## Figure 1

# Appendix B

# Constants and Basic Ideas:

# The speed of light, c = 3 x 108 m/s

- Charge in each bin = 0.25 x 10-12 C [ADC or qvt]

- Energy lost traveling through scintillator = 2 MeV/g/cm2 [This depends mildly on the type of material and the momentum of the particle.]

- Charge on 1 electron = -1.6 x 10-19 C

- Time gate is open ((t) = 40 ns [This is determined by the width of the signal.  The discriminator output is 20 ns.  (2 x 20 ns = 40 ns)]

- Research is like climbing a mountain.  The view from the top and bottom give beautiful views, but there is a lot of hard work and opportunity to get lost in, the middle.  [Julia Thompson]

# Appendix C

# Calculations:

- v = c / n: where v is the velocity in the medium, c is the speed of light and n is the index of refraction.

- Charge per 1 PE = (PE bin– pedestal bin) x (0.25 x 10-12 C / bin)

- Charge for CR = (CR bin – pedestal bin) x (0.25 x 10-12 C / bin)

- PE = PE bin – pedestal bin

- CR = CR bin – pedestal bin

- Ratio of PE/CR  = bins/ CR

Bins / PE

- Gain = number of electrons out of the photomultiplier / 1 electron converted from 1 photon.

- Gain = (PE – pedestal) bin x (0.25 x 10-12 C / bin) x (1 e- / 1.6 x 10-19 C) / 1e- converted

- Determination of expected rate:

  - Rn = 180 CR/m2 x (area of scintillatorn) in m2

  - (t = 40 ns = 40 x 10-9 s

  - Rate (R) = counts / second

  - Expected Accidental rate = R1 x R2 x ((t)

  - For more than two counters EAR =    ((t) n-1

- Efficiency of Geometric Light Collection of the Large scintillators                      (~ 45 cm x ~90 cm x ~1 cm)

  - In a scintillator approximately 1 cm thick 2 MeV are deposited per particle

  - One photon is produced per 100 eV deposited in the scintillator.

  - 2 x 106 eV x 1 photon / 100 eV = 2 x104 photons produced from 1 cosmic ray (particle)

  - 2 x 104 photons x 0.03 geometric efficiency x (reflection efficiency inside the scintillator)

  - Reflection efficiency in y and z planes is ~ (.99) n [where n is the number of bounces in the y and z planes of the scintillator, the assumption is that the photon is emitted in the middle of the counter.  Bouncing in the narrow direction, a photon travels ~ 2 widths in the z direction for very bounce.  It must travel ~ 45 cm to reach the light guide.  The critical angle is ~ 45o.

(~ 45cm/ 2 Widths / width/ bounce ~ 22 bounces]  The light that remains is  ~ (1-.01) 22 ~ (1-22(.01)) ~ 0.78

  - Efficiency ~ 0.03 x 0.78 ~ 2 %

  - (0.02) x 2 x 104 photons = 400 photons reaching the photocathode.

- Efficiency of Geometric Light Collection of the small scintillators (~15 cm x 30 cm)

  - In a scintillator approximately 1 cm thick 2 MeV are deposited per particle.

  - One photon is produced per 100 eV.

  - The small scintillators are about 0.5 cm thick.

  - (0.5) x 2 x 106 V x 1 photon / 100 eV = 1 x104 photons produced from 1 cosmic ray (particle)

  - Geometric light collection: Assume the ones that move away from the light guide never reach it ~ 0.5 and the ones whose angle are less than the critical angle are lost ~ 0.5 since the critical angle is ~ 45o.  These are the main factors (there is some attenuation and the losses due to the matching of the light guide to the scintillator and the photomultiplier is ~ 0.3.  All of these together [0.5 x 0.5 x 0.7] are ~0.18.

  - Reflection efficiency in y and z planes is ~ (.99) n [where n is the number of bounces in the y and z planes of the scintillator, the assumption is that the photon is emitted in the middle of the counter and must travel 15 cm to reach the light guide. ~ 15cm/ 1 cm/ bounces ~ 15 bounces]

  - ~ (1-.01) 8 ~ (1-15(.01)) ~ 0.85

  - Efficiency ~ 0.18 x 0.85 ~ 0.15 %

  - (0.15) x 1 x 104 photons = 1500 photons reaching the photocathode.

- Efficiency of Photomultiplier in converting photons to electrons between 5% and 25 %

  - Assuming the best quantum efficiency of 25 %, the large counters, approximately 50 to 100 electrons are available to be multiplied in the photomultiplier.

  - Assuming the best quantum efficiency of 25 %, the small counters, approximately 400 electrons are available to be multiplied in the photomultiplier.

- Light collected

  - ( Light collected in x z planes

  - ( light collected in x y and z y planes

  - Range for first integral is 0 to 2(

  - Range for the second integral is –1 to +1

  - Light collected =

Appendix D

#### DATA

Table 1 Singles Counts ordered by Counter, Voltage, and Date

|  |  |  |  |  | Expected |
| --- | --- | --- | --- | --- | --- |
|  | Date | Counter | Voltage | counts/s | Count |
| 1 | 25-Jun-03 | L1 | 0 | 0 | 76 |
| 2 | 25-Jun-03 | L1 | 1600 | 5 | 76 |
| 3 | 25-Jun-03 | L1 | 1700 | 32 | 76 |
| 4 | 25-Jun-03 | L1 | 1800 | 95 | 76 |
| 5 | 2-Jul-03 | L1 | 1800 | 481 | 76 |
| 6 | 25-Jun-03 | L1 | 1900 | 247 | 76 |
| 7 | 7-Jul-03 | L1 | 1900 | 96 | 76 |
| 8 | 7-Jul-03 | L1 | 1900 | 88 | 76 |
| 9 | 7-Jul-03 | L1 | 1900 | 93 | 76 |
| 10 | 10-Jul-03 | L1 | 1900 | 334 | 76 |
| 11 | 10-Jul-03 | L1 | 1900 | 565 | 76 |
| 12 | 11-Jul-03 | L1 | 1900 | 684 | 76 |
| 13 | 11-Jul-03 | L1 | 1900 | 753 | 76 |
| 14 | 11-Jul-03 | L1 | 1900 | 473 | 76 |
| 15 | 11-Jul-03 | L1 | 1900 | 661 | 76 |
| 16 | 11-Jul-03 | L1 | 1900 | 601 | 76 |
| 17 | 11-Jul-03 | L1 | 1900 | 560 | 76 |
| 18 | 11-Jul-03 | L1 | 1900 | 536 | 76 |
| 19 | 11-Jul-03 | L1 | 1900 | 519 | 76 |
| 20 | 11-Jul-03 | L1 | 1900 | 489 | 76 |
| 21 | 11-Jul-03 | L1 | 1900 | 446 | 76 |
| 22 | 11-Jul-03 | L1 | 1900 | 427 | 76 |
| 23 | 11-Jul-03 | L1 | 1900 | 395 | 76 |
| 24 | 25-Jun-03 | L1 | 2000 | 3409 | 76 |
| 25 | 25-Jun-03 | L1 | 2000 | 9014 | 76 |
| 26 | 7-Jul-03 | L1 | 2100 | 17812 | 76 |
| 27 | 7-Jul-03 | L1 | 2100 | 17812 | 76 |
| 28 | 7-Jul-03 | L1 | 2100 | 17538 | 76 |
| 29 | 11-Jul-03 | L2 | 2000 | 3164 | 76 |
| 30 | 11-Jul-03 | L2 | 2000 | 3419 | 76 |
| 31 | 2-Jul-03 | L4 | 1800 | 29 | 76 |
| 32 | 11-Jul-03 | L4 | 2000 | 663 | 76 |
| 33 | 11-Jul-03 | L4 | 2000 | 643 | 76 |
| 34 | 11-Jul-03 | L4 | 2000 | 646 | 76 |
| 35 | 11-Jul-03 | L4 | 2000 | 636 | 76 |
| 36 | 11-Jul-03 | L4 | 2000 | 628 | 76 |
| 37 | 2-Jul-03 | L5 | 1800 | 303 | 76 |
| 38 | 11-Jul-03 | L5 | 1900 | 10743 | 76 |

Table 1 Singles Counts ordered by Counter, Voltage, and Date

|  | Date | Counter | Voltage | Count/10s | Count/s |
| --- | --- | --- | --- | --- | --- |
| 39 | 2-Jul-03 | L6 | 1900 | 596 | 76 |
| 40 | 7-Jul-03 | L6 | 1900 | 572 | 76 |
| 41 | 7-Jul-03 | L6 | 1900 | 572 | 76 |
| 42 | 7-Jul-03 | L6 | 1900 | 583 | 76 |
| 43 | 10-Jul-03 | L6 | 2000 | 1480 | 76 |
| 44 | 10-Jul-03 | L6 | 2000 | 1592 | 76 |
| 45 | 11-Jul-03 | L6 | 2000 | 1439 | 76 |
| 46 | 7-Jul-03 | L6 | 2100 | 1877 | 76 |
| 47 | 7-Jul-03 | L6 | 2100 | 1842 | 76 |
| 48 | 7-Jul-03 | L6 | 2100 | 1817 | 76 |
| 49 | 7-Jul-03 | L6 | 2100 | 1850 | 76 |
| 50 | 24-Jun-03 | LA | 1500 | 1 | 9 |
| 51 | 24-Jun-03 | LA | 1600 | 14 | 9 |
| 52 | 24-Jun-03 | LA | 1700 | 30 | 9 |
| 53 | 24-Jun-03 | LA | 1800 | 52 | 9 |
| 54 | 2-Jul-03 | LA | 1800 | 12 | 9 |
| 55 | 24-Jun-03 | LA | 1900 | 108 | 9 |
| 56 | 24-Jun-03 | LA | 1900 | 90 | 9 |
| 57 | 24-Jun-03 | LA | 2000 | 412 | 9 |
| 58 | 10-Jul-03 | LA | 2000 | 371 | 9 |
| 59 | 10-Jul-03 | LA | 2000 | 331 | 9 |
| 60 | 11-Jul-03 | LA | 2000 | 286 | 9 |
| 61 | 11-Jul-03 | LA | 2000 | 273 | 9 |
| 62 | 11-Jul-03 | LA | 2000 | 289 | 9 |
| 63 | 24-Jun-03 | LA | 2200 | 987 | 9 |
| 64 | 25-Jun-03 | LB | 1500 | 0 | 18 |
| 65 | 25-Jun-03 | LB | 1600 | 0 | 18 |
| 66 | 25-Jun-03 | LB | 1700 | 19 | 18 |
| 67 | 25-Jun-03 | LB | 1800 | 91 | 18 |
| 68 | 10-Jul-03 | LB | 1800 | 277 | 18 |
| 69 | 10-Jul-03 | LB | 1800 | 109 | 18 |
| 70 | 11-Jul-03 | LB | 1800 | 110 | 18 |
| 71 | 25-Jun-03 | LB | 1900 | 877 | 18 |
| 72 | 2-Jul-03 | LB | 1900 | 711 | 18 |
| 73 | 25-Jun-03 | LB | 2000 | 303 | 18 |

## Table 2 Coincidences

|  |  |  |  |  |  |  |  |  |  |  |  |  | Observed | Observed |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Also |  |  |  |  |  |  |  |  | Bins/(PE-PED) | Bins/(CR-PED) |  |
|  |  |  |  | Triggered | Evaluation |  | qvt |  |  |  |  |  | Including | Including |  |
| No. |  | Date | Counter | On | Voltage | Atten | Pedestal | PE peak | PE -PED | CR peak | CR-PED | Gain | Attenuation | Attenuation | PE / CR |
| 1 |  | 03-Jul-03 | L1 | L6 | 2100 | 1 | 21 | 45 | 24 | 397 | 376 | 3.8E+07 | 24 | 376 | 16 |
| 2 |  | 07-Jul-03 | L1 | ? | 2100 | 1 | 19 | 42 | 23 | 289 | 270 | 3.6E+07 | 23 | 270 | 12 |
| 3 |  | 03-Jul-03 | L2 |  | 2100 | 5 | 41.5 | 45.5 | 4 | 221 | 179.5 | 3.1E+07 | 20 | 897.5 | 45 |
| 4 |  | 07-Jul-03 | L3 | LB, L1, L6 | 2000 | 1 | 22 | 76 | 54 | 463 | 441 | 8.4E+07 | 54 | 441 | 8 |
| 5 |  | 08-Jul-03 | L3 | L3, L6 | 2000 | 5 | 40 | 50 | 10 | 256 | 216 | 7.8E+07 | 50 | 1080 | 22 |
| 6 |  | 08-Jul-03 | L3 | L1, L6, LB, L3 | 2000 | 5 | 40 | 50 | 10 | 105 | 65 | 7.8E+07 | 50 | 325 | 7 |
| 7 |  | 08-Jul-03 | L3 | L1, L6, LA, L4 | 2000 | 5 | 40 | 50 | 10 | 256 | 325 | 7.8E+07 | 50 | 1080 | 22 |
| 8 |  | 10-Jul-03 | L4 | LA, L4 | 2000 | 1 | 22 | 44 | 22 | 68 | 46 | 3.4E+07 | 22 | 46 | 2 |
| 9 |  | 18-Jul-03 | L4 | L1, L4, L6 | 2000 | 1 | 16 | 38 | 22 | 82 | 66 | 3.4E+07 | 22 | 66 | 3 |
| 10 |  | 18-Jul-03 | L4 | L1, L4, L6 | 2000 | 5 | 35 | 39 | 4 | 48 | 13 | 3.1E+07 | 20 | 65 | 3 |
| 11 |  | 10-Jul-03 | L4 | LA, L1 | 2100 | 1 | 22 | 62 | 40 | 94 | 72 | 6.3E+07 | 40 | 72 | 2 |
| 12 |  | 18-Jul-03 | L5 | L1, L6 | 1900 | 1 | 31 | 47 | 16 | 159 | 128 | 2.5E+07 | 16 | 128 | 8 |
| 13 |  | 18-Jul-03 | L5 | L1, L6 | 1900 | 1 | 32 | 47 | 15 | 160 | 128 | 2.3E+07 | 15 | 128 | 9 |
| 14 |  | 08-Jul-03 | L5 | L1, L6 | 2000 | 5 | 40 | 49 | 9 | 189 | 149 | 7.0E+07 | 45 | 745 | 17 |
| 15 |  | 08-Jul-03 | L5 | L1 | 2000 | 5 | 40 | 49 | 9 | 189 | 149 | 7.0E+07 | 45 | 745 | 17 |
| 16 |  | 08-Jul-03 | L6 | L1, L6 | 2000 | 5 | 40 | 50 | 10 | 110 | 70 | 7.8E+07 | 50 | 350 | 7 |
| 17 |  | 24-Jun-03 | LA | S1 | 2200 | 1 | 41 | 51 | 10 | 890 | 849 | 1.6E+07 | 10 | 849 | 85 |
| 18 |  | 25-Jun-03 | LA | L6 | 2200 | 1 | 40 | 50 | 10 | 986 | 946 | 1.6E+07 | 10 | 946 | 95 |
| 19 |  | 08-Jul-03 | LA | All others? | 2200 | 1 | 41 | 51 | 10 | 446 | 405 | 1.6E+07 | 10 | 405 | 41 |
| 20 |  | 24-Jun-03 | LB | L1 | 2100 | 5 | 39 | 53 | 14 | 494 | 455 | 1.1E+08 | 70 | 2275 | 33 |
| 21 |  | 24-Jun-03 | LB | ? | 2100 | 5 | 41 | 53 | 12 | 465 | 424 | 9.4E+07 | 60 | 2120 | 35 |
| 22 |  | 25-Jun-03 | LB | LB, L1 | 2100 | 5 | 39 | 57 | 18 | 494 | 455 | 1.4E+08 | 90 | 2275 | 25 |
| 23 |  | 25-Jun-03 | LB | L1 | 2100 | 5 | 40 | 57 | 17 | 447 | 407 | 1.3E+08 | 85 | 2035 | 24 |

Table 2 Coincidences Con’t.

|  |  |  |  |  |  |  |  |  |  | Expected | Expected |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | 2000 V |  | Expected | Expected | PE+ ADC PED | CR+ ADC PED |  |  |
|  |  |  | Difference in | Expected | Expected | Minus | Final | Bins/(PE-PED) | Bins/(CR-PED) | Of ~10 at | Of ~ 10 at | Also |  |
|  |  |  | Voltage from | Bins/PE | Bins/CR peak | Final | Voltage | At final | At final | Final | Final | Triggered | PE/CR |
| No | Date |  | 2000 V | At 2000 V | At 2000 V | Voltage | Used | Voltage | Voltage | Voltage | Voltage | On |  |
| 1 | 03-Jul-03 | L1 | -100 | 12 | 188 | 100 | 1900 | 6 | 94 | 16 | 104 | L6 | 16 |
| 2 | 07-Jul-03 | L1 | -100 | 11.5 | 135 | 100 | 1900 | 6 | 68 | 16 | 78 | ? | 12 |
| 3 | 03-Jul-03 | L2 | -100 | 10 | 448.75 | 0 | 2000 | 10 | 449 | 20 | 459 |  | 45 |
| 4 | 07-Jul-03 | L3 | 0 | 54 | 441 | 100 | 1900 | 27 | 221 | 37 | 231 | LB, L1, L6 | 8 |
| 5 | 08-Jul-03 | L3 | 0 | 50 | 1080 | 100 | 1900 | 25 | 540 | 35 | 550 | L3, L6 | 22 |
| 6 | 08-Jul-03 | L3 | 0 | 50 | 325 | 100 | 1900 | 25 | 163 | 35 | 173 | L1, L6, LB, L3 | 7 |
| 7 | 08-Jul-03 | L3 | 0 | 50 | 1080 | 100 | 1900 | 25 | 540 | 35 | 550 | L1, L6, LA, L4 | 22 |
| 8 | 10-Jul-03 | L4 | 0 | 22 | 46 | 0 | 2000 | 22 | 46 | 32 | 56 | LA, L4 | 2 |
| 9 | 18-Jul-03 | L4 | 0 | 22 | 66 | 0 | 2000 | 22 | 66 | 32 | 76 | L1, L4, L6 | 3 |
| 10 | 18-Jul-03 | L4 | 0 | 20 | 65 | 0 | 2000 | 20 | 65 | 30 | 75 | L1, L4, L6 | 3 |
| 11 | 10-Jul-03 | L4 | -100 | 20 | 36 | 0 | 2000 | 20 | 36 | 30 | 46 | LA, L1 | 2 |
| 12 | 18-Jul-03 | L5 | 100 | 32 | 256 | 100 | 1900 | 16 | 128 | 26 | 138 | L1, L6 | 8 |
| 13 | 18-Jul-03 | L5 | 100 | 30 | 256 | 100 | 1900 | 15 | 128 | 25 | 138 |  | 9 |
| 14 | 08-Jul-03 | L5 | 0 | 45 | 745 | 100 | 1900 | 23 | 373 | 33 | 383 | L1, L6 | 17 |
| 15 | 08-Jul-03 | L5 | 0 | 40 | 745 | 100 | 1900 | 20 | 373 | 30 | 383 | L1 | 19 |
| 16 | 08-Jul-03 | L6 | 0 | 50 | 350 | 0 | 2000 | 50 | 350 | 60 | 360 | L1, L6 | 7 |
| 17 | 24-Jun-03 | LA | -200 | 2.5 | 212.25 | 0 | 2000 | 3 | 212 | 13 | 222 | S1 | 85 |
| 18 | 25-Jun-03 | LA | -200 | 2.5 | 236.5 | 0 | 2000 | 3 | 237 | 13 | 247 | L6 | 95 |
| 19 | 08-Jul-03 | LA | -200 | 2.5 | 101.25 | 0 | 2000 | 3 | 101 | 13 | 111 | ? | 41 |
| 20 | 24-Jun-03 | LB | -100 | 35 | 1137.5 | 200 | 1800 | 9 | 284 | 19 | 294 | L1 | 33 |
| 21 | 24-Jun-03 | LB | -100 | 30 | 1060 | 200 | 1800 | 8 | 265 | 18 | 275 | ? | 35 |
| 22 | 25-Jun-03 | LB | -100 | 45 | 2275 | 200 | 1800 | 11 | 569 | 21 | 579 | LB, L1 | 51 |
| 23 | 26-Jun-03 | LB | -100 | 42.5 | 2035 | 200 | 1800 | 11 | 509 | 21 | 519 | L1 | 48 |

Table 3 The Expected PE and CR Measurements for the ADC plots

|  |  |  |  |  |  |  | Expected | Expected |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | PE+ ADC PED | CR+ ADC PED |  |  |  |  |
|  |  |  | Final |  |  |  | Of ~10 at | Of ~ 10 at |  |  | Also |  |
|  |  |  | Used | Expected | Expected |  | Final | Final | Where PE |  | Triggered |  |
| No. | Date | Counter | Voltage | Bins/(PE-PED) | Bins/(CR-PED) | PE/CR | Voltage | Voltage | Measured | Counter | On |  |
| 1 | 3-Jul-03 | L1 | 1900 | 6 | 94 | 16 | 16 | 104 | Middle | L1 | L6 | LA near PMT of odd numbered counters |
| 2 | 7-Jul-03 | L1 | 1900 | 6 | 68 | 12 | 16 | 78 | ? | L1 | ? |  |
| 3 | 3-Jul-03 | L2 | 2000 | 10 | 449 | 45 | 20 | 459 | ? | L2 | ? |  |
| 4 | 7-Jul-03 | L3 | 1900 | 27 | 221 | 8 | 37 | 231 | Far | L3 | LB, L1, L6 |  |
| 5 | 8-Jul-03 | L3 | 1900 | 25 | 540 | 22 | 35 | 550 | Middle | L3 | L6 |  |
| 6 | 8-Jul-03 | L3 | 1900 | 25 | 163 | 7 | 35 | 173 | Far | L3 | L1, L6, LB |  |
| 7 | 8-Jul-03 | L3 | 1900 | 25 | 540 | 22 | 35 | 550 | Near | L3 | L1, L6, LA, L4 | LA near PMT of odd numbered counters |
| 8 | 10-Jul-03 | L4 | 2000 | 22 | 46 | 2 | 32 | 56 | Far | L4 | LA | LA near PMT of odd numbered counters |
| 9 | 18-Jul-03 | L4 | 2000 | 22 | 66 | 3 | 32 | 76 | Middle | L4 | L1, L6 |  |
| 10 | 18-Jul-03 | L4 | 2000 | 20 | 65 | 3 | 30 | 75 | Middle | L4 | L1, L6 |  |
| 11 | 10-Jul-03 | L4 | 2000 | 20 | 36 | 2 | 30 | 46 | Far | L4 | LA, L1 |  |
| 12 | 18-Jul-03 | L5 | 1900 | 16 | 128 | 8 | 26 | 138 | Middle | L5 | L1, L6 |  |
| 13 | 18-Jul-03 | L5 | 1900 | 15 | 128 | 9 | 25 | 138 | ? | L5 | ? |  |
| 14 | 8-Jul-03 | L5 | 1900 | 23 | 373 | 17 | 33 | 383 | Middle | L5 | L1, L6 |  |
| 15 | 8-Jul-03 | L5 | 1900 | 20 | 373 | 19 | 30 | 383 | Near | L5 | L1 |  |
| 16 | 8-Jul-03 | L6 | 2000 | 50 | 350 | 7 | 60 | 360 | Middle | L6 | L1 |  |
| 17 | 24-Jun-03 | LA | 2000 | 3 | 212 | 85 | 13 | 222 | ? | LA | S1 | LA near PMT of odd numbered counters |
| 18 | 25-Jun-03 | LA | 2000 | 3 | 237 | 95 | 13 | 247 | ? | LA | L6 | LA near PMT of odd numbered counters |
| 19 | 8-Jul-03 | LA | 2000 | 3 | 101 | 41 | 13 | 111 | ? | LA | ? | LA near PMT of odd numbered counters |
| 20 | 24-Jun-03 | LB | 1800 | 9 | 284 | 33 | 19 | 294 | ? | LB | L1 | LB near PMT of even numbered counters |
| 21 | 24-Jun-03 | LB | 1800 | 8 | 265 | 35 | 18 | 275 | Centered | LB | ? | LB near PMT of even numbered counters |
| 22 | 25-Jun-03 | LB | 1800 | 11 | 569 | 51 | 21 | 579 | Centered | LB | LB, L1 | LB near PMT of even numbered counters |
| 23 | 25-Jun-03 | LB | 1801 | 11 | 509 | 48 | 21 | 519 | Centered | LB | L1 | LB near PMT of even numbered counters |

## Table 4 Overlap

## Study for LB and L1

|  | 1800 V |  |  | 1800 V |  |  |  |  |  |  | Average |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Overlap |  |  |  | Average | L1 Singles | Coincidence counts / s for | Coincidence Rates/s | Expected | Expected | Accidental |  |
| In cm | LB Singles Counts/s | For LB | Counts/s | LB and L1 | For LB and L1 | Rate LB/s | Rate L1/s | Rate/s |  |
| 45 | 434.2 | 237.9 | 247.5 | 307 | 104.8 | 5.5 | 6.4 | 6 | 4.5 | 5.1 | 6.8 | 5.7 | 8 | 71 | 1.28E-03 |  |
| 24 | 175 |  |  | 175 | 95.2 | 2.9 | 2.8 | 2.7 |  |  |  | 2.8 | 8 | 71 | 6.66E-04 |  |
| 10 | 98 |  |  | 98 | 97.6 | 1.5 | 1.7 | 1.1 |  |  |  | 1.4 | 8 | 71 | 3.83E-04 |  |
| 5 | 99.5 |  |  | 99.5 | 405.7 | 0.8 | 0.8 | 0.5 |  |  |  | 0.7 | 8 | 71 | 1.61E-03 |  |
| 0 | 94.4 |  |  | 94.4 | 132.4 | 0.5 | 0.3 | 0.3 |  |  |  | 0.4 | 8 | 71 | 5.00E-04 |  |
| -150 | 268.1 | 107 | 168.8 | 181 | 125.6 | 0.1 | 0 | 0 |  |  |  | 0.0 | 8 | 71 | 9.11E-04 |  |
|  | 2100 V |  |  | 2100 V |  |  |  |  |  |  | Average |  |  |  | Coincidence |
| Overlap |  |  |  | Average | L1 Singles | Coincidence counts / s for | Coincidence Rates/s | Expected | Expected | Accidental | Minus |
| In cm | LB Singles Counts/s | For LB | Counts/s | LB and L1 | For LB and L1 | Rate LB/s | Rate L1/s | Rate/s | Accidentals |
| 0 | 5924 |  |  | 5923.6 | 44005 | 178 | 204 | 163 | 158 | 202 |  | 18.1 | 8 | 71 | 10.43 | 7.7 |

## Table 5 Unreliable or Irreproducible Data

|  |  |  |  |  |  |  |  |  |  |  | Observed | Observed |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  | Bins/(PE-PED) | Bins/(CR-PED) |  |
|  |  |  |  |  |  |  |  |  |  |  | Including | Including |  |
|  |  | Counter | Voltage | Attend | Pedestal | PE peak | PE - PED | CR peak | CR - PED | Gain | Attenuation | Attenuation | PE/CR |
| 1 | 08-Jul-03 | L4 | 2000 | 5 | 40 | 45 | 5 | 207 | 167 | 7.8E+06 | 25 | 835 | 33.4 |
| 2 | 08-Jul-03 | L5 | 2000 | 5 | 40 | 49 | 9 | 189 | 149 | 1.4E+07 | 45 | 745 | 16.6 |
| 3 | 07-Jul-03 | L6 | 2100 | 1 | 22 | 24 | 2 | 115 | 93 | 3.1E+06 | 2 | 93 | 46.5 |

|  |  |  |  |  |  |  |  |  | Expected | Expected |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Expected | Expected |  | PE + ADC PED | CR + ADC PED |  |
|  |  | Difference in | Expected | Expected | Final | Bins (PE - PED) | Bins (CR - PED) |  | Of ~10 at | Of ~10 at |  |
|  |  | Voltage from | Bins/PE | CR peak | Voltage | Including | Including |  | Determined | Determined |  |
|  |  | 2000 V | At 2000 V | At 2000 V | Used | Attenuation | Attenuation | PE/CR | Voltage | Voltage | PE/CR |
| 1 | L4 | 0 | 25 | 835 | 2000 | 25 | 835 | 835 | 35 | 2000 | 57.1 |
| 2 | L5 | 0 | 45 | 745 | 2000 | 45 | 745 | 745 | 55 | 2000 | 36.4 |
| 3 | L6 | -100 | 1 | 46.5 | 2000 | 1 | 46.5 | 46.5 | 11 | 2000 | 181.8 |

Appendix E

#### Statistical Analysis of Data

| SUMMARY OUTPUT: COUNTER L A |
| --- |
| Regression Statistics |  |  |  |  |  |  |  |
| Multiple R | 0.949066596 |  |  |  |  |  |  |  |
| R Square | 0.900727404 |  |  |  |  |  |  |  |
| Adjusted R Square | 0.892454687 |  |  |  |  |  |  |  |
| Standard Error | 0.631518907 |  |  |  |  |  |  |  |
| Observations | 14 |  |  |  |  |  |  |  |
| ANOVA |  |  |  |  |  |  |  |  |
|  | df | SS | MS | F | Significance F |  |  |  |
| Regression | 1 | 43.42281308 | 43.42281 | 108.8793 | 2.2575E-07 |  |  |  |
| Residual | 12 | 4.785793552 | 0.398816 |  |  |  |  |  |
| Total | 13 | 48.20860663 |  |  |  |  |  |  |
|  | Coefficients | Standard Error | t Stat | P-value | Lower 95% | Upper 95% | Lower 95.0% | Upper 95.0% |
| Intercept | -13.88589479 | 1.769380291 | -7.84789 | 4.57E-06 | -17.7410432 | -10.0307 | -17.741 | -10.03074638 |
| X Variable 1 | 0.009746148 | 0.000934029 | 10.43452 | 2.26E-07 | 0.007711074 | 0.011781 | 0.007711 | 0.011781223 |

| SUMMARY OUTPUT: COUNTER LB |
| --- |
| Regression Statistics |  |  |  |  |  |  |  |
| Multiple R | 0.9313527 |  |  |  |  |  |  |  |
| R Square | 0.867417851 |  |  |  |  |  |  |  |
| Adjusted R Square | 0.850845082 |  |  |  |  |  |  |  |
| Standard Error | 1.289877634 |  |  |  |  |  |  |  |
| Observations | 10 |  |  |  |  |  |  |  |
| ANOVA |  |  |  |  |  |  |  |  |
|  | df | SS | MS | F | Significance F |  |  |  |
| Regression | 1 | 87.08238455 | 87.08238 | 52.33995 | 8.93798E-05 |  |  |  |
| Residual | 8 | 13.31027448 | 1.663784 |  |  |  |  |  |
| Total | 9 | 100.392659 |  |  |  |  |  |  |
|  | Coefficients | Standard Error | t Stat | P-value | Lower 95% | Upper 95% | Lower 95.0% | Upper 95.0% |
| Intercept | -33.7998666 | 5.202111218 | -6.49734 | 0.000189 | -45.79596433 | -21.8038 | -45.796 | -21.8038 |
| X Variable 1 | 0.021078375 | 0.002913537 | 7.234635 | 8.94E-05 | 0.014359743 | 0.027797 | 0.01436 | 0.027797 |

| SUMMARY OUTPUT: COUNTER L 1 |
| --- |
| Regression Statistics |  |  |  |  |  |  |  |
| Multiple R | 0.941955986 |  |  |  |  |  |  |  |
| R Square | 0.88728108 |  |  |  |  |  |  |  |
| Adjusted R Square | 0.882945737 |  |  |  |  |  |  |  |
| Standard Error | 0.749190889 |  |  |  |  |  |  |  |
| Observations | 28 |  |  |  |  |  |  |  |
| ANOVA |  |  |  |  |  |  |  |  |
|  | df | SS | MS | F | Significance F |  |  |  |
| Regression | 1 | 114.8742596 | 114.8743 | 204.6623 | 7.76705E-14 |  |  |  |
| Residual | 26 | 14.59346168 | 0.561287 |  |  |  |  |  |
| Total | 27 | 129.4677213 |  |  |  |  |  |  |
|  | Coefficients | Standard Error | t Stat | P-value | Lower 95% | Upper 95% | Lower 95.0% | Upper 95.0% |
| Intercept | -24.2588477 | 2.122311168 | -11.4304 | 1.22E-11 | -28.62132364 | -19.8964 | -28.6213 | -19.8964 |
| X Variable 1 | 0.016034733 | 0.001120838 | 14.30602 | 7.77E-14 | 0.013730816 | 0.018339 | 0.013731 | 0.018339 |

| SUMMARY OUTPUT: COUNTER L 6 |
| --- |
| Regression Statistics |  |  |  |  |  |  |  |
| Multiple R | 0.946788011 |  |  |  |  |  |  |  |
| R Square | 0.896407538 |  |  |  |  |  |  |  |
| Adjusted R Square | 0.884897265 |  |  |  |  |  |  |  |
| Standard Error | 0.18545275 |  |  |  |  |  |  |  |
| Observations | 11 |  |  |  |  |  |  |  |
| ANOVA |  |  |  |  |  |  |  |  |
|  | df | SS | MS | F | Significance F |  |  |  |
| Regression | 1 | 2.678467693 | 2.678468 | 77.87891 | 1.00239E-05 |  |  |  |
| Residual | 9 | 0.309534503 | 0.034393 |  |  |  |  |  |
| Total | 10 | 2.988002196 |  |  |  |  |  |  |
|  | Coefficients | Standard Error | t Stat | P-value | Lower 95% | Upper 95% | Lower 95.0% | Upper 95.0% |
| Intercept | -4.528631502 | 1.312540567 | -3.45028 | 0.007272 | -7.497806811 | -1.55946 | -7.49781 | -1.55946 |
| X Variable 1 | 0.005786264 | 0.000655674 | 8.824903 | 1E-05 | 0.004303024 | 0.00727 | 0.004303 | 0.00727 |

## Appendix F

#### Graphs

lstack ADC Plots - PE Peaks

lstack ADC Plots – CR Peaks

#### Singles Counts by Counter versus Voltage and by Date

### Typical qvt Plots

Appendix G

Glossary of Terms

## Accelerators

A device used to produce high-energy high-speed beams of charged particles.

## ADC

## Analog Digital Converter

## Attenuation

Radio logically; it is the reduction of the intensity of radiation upon passage through a medium.  The attenuation is caused by absorption and scattering.

## Anode

## The positive terminal

## Baryon

A hadron made from a basic structure of three quarks.  The proton and neutron are both baryons.

## Bremsstrahlung

X-rays emitted when a charged particle (such as an electron) is decelerated by passing through matter.  The word bremsstrahlung is German for “braking radiation”.

Cerenkov Radiation

A charged particle emits Cerenkov radiation (light) in a cone around its direction of travel when it travels through any medium faster than the speed of light through that medium.

## Coincidence

The occurrence of events that happen at the same time.

## CR

Cosmic Rays

## Doped

A substance added in trace amount to another material.

## Dynode

An electrode, in an electron tube, that functions to produce secondary emissions of electrons.

eV (electron volt)

The basic unit of energy used in high energy physics.  It is the energy gained by one electron when it moves through a potential difference of one volt.  By definition, an eV is equivalent to 1.6 x 10-19 joules.

Excitation

The addition of energy to a system, transferring it from its ground state to an excited state.  Excitation of a nucleus, an atom, or a molecule can result from absorption of photons or from inelastic collisions with other particles.

Fluors

Materials, which give of the kind of luminescence in which the emanation of light continues only as long as the excitation lasts and in which the emission of radiation follows the excitation almost instantaneously.

GeV (Giga Electron Volt)

Unit of energy equal to that acquired by a particle with one electronic charge passing through a potential difference of one billion volts.  1 GeV = 109 eV

Hadron

Any particle made of quarks and gluons, i.e. a meson or a baryon

High Energy Physics

A branch of science that tries to understand the interactions of the fundamental particles, such as electrons, photons, neutrons, and protons (and many others that can be created).  Cosmic rays have higher energies than can be produced in accelerators.

Lepton

A fundamental matter particle that does not participate in strong interactions.  The charge leptons are the electrons (e) the muons ((), the tau ((), and their antiparticles.

Meson

A hadron with the basic structure of one quark and one antiquark.

Momentum

The mass times the velocity of an object.  This definition is modified for any particle moving close to the speed of sound.

Muon

The second lepton (in order of increasing mass) with an electric charge of –1.

MeV (Mega Electron Volt)

1 MeV = 1 x 106 eV

Nucleon

A proton, neutron, and other particles formed as a result of bombardment of a nucleus with high-energy particles.

Nucleus

A collection of protons and neutrons that form the core of an atom.

Particle

In “particle physics”, a subatomic object with definite mass and charge.

PE

Photoelectron

Photon

The carrier particle of the electromagnetic interactions.  Depending on its frequency (and therefore energy) photons can have different names such as visible light, X-rays, and gamma rays.  They are uncharged particles without mass that carry energy.

PM

A Photomultiplier

Relativistic

Traveling at a significant fraction of the speed of light.

Shower Electrons can create photons by interaction with a medium.  In a similar way, photons can create electrons and their antiparticles, positrons, by interacting with a medium.  So, imagine a very high-energy electron impinging on some material.  The electron can set photons into motion and these photons can, in turn set electrons and positrons into motion and this process can continue to repeat.  One high-energy electron can set thousands of particles into motion.  The particle creation process only stops when the energy runs out.

Steradian

The unit for a solid angle, i.e. three-dimensional angle.

Tau

The third charged lepton (in order of increasing mass), with electric charge of one.

TDC

Time Digital Converter

## TeV  (Tetra Electron Volt)

1 x 1012 eV

Appendix H

Citations:

Godwin, Mark Debbie; Paper for CosRay/RET; 2003

Gremmelsbacher, Debbie; Paper for CosRay/RET; Cosmic Ray Detection, July 9, 2003

Particle Physics Booklet, July 2000, Springer.

Thomas, Drew; Paper for Cosmic Ray Project, REUP-FOM/SIUE 2001

# Footnotes

8/6/2003 4:48 PM

See Appendix A Figure 1

Particle Physics Booklet; July 2000; Springer ( p. 180)

See Appendix G Glossary for technical terms

see Appendix C Calculations

Particle Physics Booklet; July 2000; Springer (p. 205)

See Appendix C Calculations

See Appendix A Figure 2

See Appendix A Figures 3, 4, 5, and 6

See Appendix A Figure 7

The dtake program was written by Elizabeth Weber in the summer of 2001.  It uses Fortran and Physics Analysis Workstation [PAW]

See Appendix C

See Appendix A Figure 3

6 See Appendix D Table 4

See Appendix F Graphs 1 and 2

See Appendix D Table 1

See Appendix F: Graphs  overlap graph page 38

See Appendix D Data: Table 4

See Appendix D:  Table 2

Analysis performed by Thomas W. Langford see Appendix E Statistical Analysis

Graph prepared by Julia Thompson see Appendix F Graphs p 33

Appendix D Graphs:  Table 4

Julia Thompson in a private communication.

For further studies using dtake see ‘Godwin, Mark, PhD  Cosmic Ray study 2003

See Appendix A Figure 3

see graphs in Appendix E.

See Table 1 Figures 9 and 10

See Appendix F pages 32 and 33

Appendix D, Table 4 and Appendix F the first two graphs

Particle Physics Booklet; July 2000; Springer; pp. 270-271

Op. Cit. p. 205

Thomas

see Appendix A Figure 8

Definitions from http://www2.slac.stanford.edu/vvc/glossary.html; Webster’s Ninth Collegiate Dictionary; and Glossary of Chemical Terms by Hampel & Hawley; Van Nostrand Reinhold Company, New York  (1976)

# Text boxes

Figure 2 path of light through the scintillator

critical angle

scintillator

Normal

photon emitted

photon leaves

the

scintillator

L1

L3

L5

Figure 3: Arrangement of the six large counters.

Scintillators

L2

L4

L6

Light guides and photomultipliers

Light guides and photomultipliers

Dynode

Anode

High Voltage

Dynode

Anode

High                     Voltage

Figure 4 The Configurations of the End of a photomultiplier (PM)

opens gate

High Voltage Source

Scintillator     Light      PM

Guide

ADC

TDC

Computer

PM sends variable sized signals.

Legend

Analog signal

Digital Signal

Discriminator (output is –0.5 V)

Coincidence

Signal Stops TDC

Signal Starts TDC

## Figure 5   Arrows with solid lines represent cables.  Arrows with dotted lines are comments

Coincidence actually has input for 4 cables only.

Discriminator

Display

Coincidence

TDC

ADC

Counter

Computer

Figure 6 Wiring Diagram of dynodes.  All anodes go directly to the ADC.  From the discriminator all signals go to the TDC.  Variable size pulses enter the discriminator.  The discriminator output standardizes the signal, ~ -0.5V, square, and adjustable ~ 20 ns wide.

Z

X

Y

Width, W

2 W

Figure 8 Showing the 3-dimensional internal reflection of light from a proton originating in the center of the scintillator.  Not to scale.  See Figure 2 for further information.

Figure 7 Connections for timing of cables.

Pulse Generator

Cable to be tested

oscilloscope

Figure 9:  Side view of the arrangement of the six large counters with LA.

L2

L4

L6

L1

L3

L5

Light guides and photomultipliers

Light guides and photomultipliers

Scintillators

With LA on top perpendicular to the rest of the stack

Figure 10: Top view of  the stack with LA’s scintillator centered over the scintillators of the stack.

L1 hv  (kv)