## Slide 1
Geodesy and Map Projections
Borrowed and expanded by Joe Naumann, UMSL

## Slide 2
What is a Map Projection?
It is how we represent a three dimensional Earth on a flat piece of paper
However…
The process of transferring information from the Earth to a map causes every projection to distort at least one aspect of the real world – either shape, area, distance, or direction.

## Slide 3: Is this a “good” map of the Earth?
Notes: Rhumb line—A rhumb line is a line on the surface of the Earth cutting all meridians at the same angle. A rhumb line shows true direction. Parallels and meridians, which also maintain constant true directions, may be considered special cases of the rhumb line. A rhumb line is a straight line on a Mercator projection. A straight rhumb line does not show the shortest distance between points unless the points are on the Equator or on the same meridian. A navigator can proceed between any two points along a rhumb line by maintaining a constant bearing, or compass direction.

## Slide 4
Mercator Projection and the “Greenland Problem”
Also known as Northern Hemisphere dominant projection

## Slide 5: How about this?
Infamous Peters projection of 1974 - Equal Area, True Direction
Shape (conformality) and Distance Not Preserved

## Slide 6: The Answer  It depends
A “good” map is one that is being successfully used for its intended purpose and was created in a precise and accurate manner
Always a trade-off in errors
  Shape (Conformal)
  Distance
  Area
  Direction (Local angles)
Can only keep one or two of these accurate
OR compromise between all four
Errors may not be significant for small study areas but they do exist

## Slide 7
Robinson Projection -- a compromise projection

## Slide 8
Mercator Maps used as Charts in Navigation (Ships and Planes)
Shortest distance between two points????

## Slide 9: Basic Definitions
Geodesy - The science of determining the size and shape of the earth and the precise location of points on its surface.
Map Projection - the transformation of a curved earth to a flat map.
Coordinate systems – Any set of numbers, usually in sets of two or three, used to determine location relative to other locations in two or three dimensions

## Slide 10: Types of Coordinate Systems
(1) Global Cartesian coordinates (x,y,z): A system for the whole earth
(2) Geographic coordinates (f, l, z)
(3) Projected coordinates (x, y, z) on a local area of the earth’s surface
The z-coordinate in (1) and (3) is defined geometrically; in (2) the z-coordinate is defined gravitationally

## Slide 11: Global Cartesian Coordinates (x,y,z)
O
X
Z
Y
Greenwich
Meridian
Equator
•
Extremely cumbersome and difficult to relate to other locations when
translated to two dimensions.

## Slide 12: Geographic Coordinates (Latitude and Longitude) (f, l, z)
Latitude (f) and Longitude (l) defined using an ellipsoid, an ellipse rotated about an axis
Elevation (z) defined using geoid, a surface of constant gravitational potential
Earth datums define standard baseline values of the ellipsoid and geoid (more on this later….)
Usually used in general purpose atlases and maps and textbooks.

## Slide 13: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 14: Latitude and Longitude
Lines of latitude are called “parallels”
Lines of longitude are called “meridians”
The Prime Meridian passes through Greenwich, England

## Slide 15: Latitude and Longitude in North America
90 W
120 W
60 W
30 N
0 N
60 N

## Slide 16: Length on Meridians and Parallels
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 17: How Do We Define the Shape of the Earth?
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles

## Slide 18: Ellipsoid or Spheroid Rotate an ellipse around an axis
O
X
Z
Y
a
a
b
Rotational axis

## Slide 19
Selection of the Spheroid is what determines
the SIZE of the Earth

## Slide 20: Horizontal Earth Datums (Making sure we are where we think we are….)
What is a datum????
An earth datum is defined by a specific ellipse and an axis of rotation
NAD27 (North American Datum of 1927) uses the Clarke (1866) ellipsoid on a non geocentric axis of rotation
NAD83 (NAD,1983) uses the GRS80 ellipsoid on a geocentric axis of rotation
WGS84 (World Geodetic System of 1984) uses GRS80, almost the same as NAD83

## Slide 21: Representations of the Earth
Earth surface
Ellipsoid
Sea surface
Geoid
Mean Sea Level is a surface of constant
gravitational potential called the Geoid
Since the Geoid varies due to local anomalies, we must approximate it with a ellipsoid

## Slide 22: Geoid and Ellipsoid
Ocean
Geoid
Earth surface
Ellipsoid
Gravity Anomaly

## Slide 23: North American Datum of 1927 (a very common horizontal datum – “old” data)
1866 Spheroid
(Clarke)
Geoid
Earth surface
Meades Ranch, Kansas
Spheroid
Center
Mass Center of Earth
Uses the Clarke 1866 Spheroid which minimizes error between the spheroid
and the geoid at Meades Ranch, Kansas. (The center of the U.S.; unfortunately,
not the world.)

## Slide 24: North American Datum of 1983 (a very common horizontal datum – “newer” data)
GRS80 Ellipsoid
Geoid
Earth surface
Meades Ranch, Kansas
Ellipsoid
Center
Mass Center of Earth
Uses the GRS80 Spheroid which minimizes error between the spheroid
and the geoid on average around the world. (Resulting in a spheroid center much closer to the mass center of the Earth.)

## Slide 25: Vertical Earth Datums
A vertical datum defines the “zero reference” point for elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
Takes into account a map of gravity anomalies between the ellipsoid and the geoid which are relatively constant.
Ocean
Geoid
Earth surface
Ellipsoid
Gravity Anomaly

## Slide 26: Map Projection
Curved Earth
Geographic coordinates: f, l
(Latitude & Longitude)
Flat Map
Cartesian coordinates: x,y
(Easting & Northing)
Notes: DRM

## Slide 27: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 28: Geographic and Projected Coordinates
(f, l)
(x, y)
Map Projection

## Slide 29: Projection onto a Flat Surface (Three Broad Classes by Light Source)

## Slide 30
Gnomonic Projection

## Slide 31
Stereographic Projection

## Slide 32
Orthographic Projection

## Slide 33
World from Space – Orthographic Projection

## Slide 34: Types of Projections

## Slide 35: Types of Projections
Equal Area: maintains accurate relative sizes. Used for maps that show distributions or other phenomena where showing area accurately is important. Examples: Lambert Azimuthal Equal-Area, the Albers Equal-Area Conic. Often used for small scale world maps or hemispheric maps.
Conformal: maintains angular relationships and accurate shapes over small areas. Used where angular relationships are important, such as for navigational or meteorological charts. Examples: Mercator, Lambert Conformal Conic. Easier for younger students to learn the continents by shape.
Equidistant: maintains accurate distances from the center of the projection or along given lines. Used for radio and seismic mapping, and for navigation. Examples: Equidistant Conic, Equirectangular.
Azimuthal or Zenithal: maintains accurate directions (and therefore angular relationships) from a given central point. Used for aeronautical charts and other maps where directional relationships are important. Examples: Gnomonic projection, Lambert Azimuthal Equal-Area. Often used for maps of countries or large regions of continents
View maps critically: Does this map show the selected information accurately or does it show a bias of its maker (has compromised accuracy)?

## Slide 36: Conic Projections (Albers, Lambert)
The lines where the cone is tangent or secant are the places with the least distortion.

## Slide 37: Planar or Azimuthal (Lambert)

## Slide 38: Cylindrical Projections (Mercator)
Transverse
Oblique
The lines where the cylinder is tangent or secant are the places with the least distortion.

## Slide 39: Mercator Projections

## Slide 40: Projections Preserve Some Earth Properties
Area - correct earth surface area (Albers Equal Area) important for mass balances
Shape - local angles are shown correctly (Lambert Conformal Conic)
Direction - all directions are shown correctly relative to the center (Lambert Azimuthal Equal Area)
Distance - preserved along particular lines
Some projections preserve two properties
Some projections preserve none of the above but attempt to minimize distortions in all four
The degree and kinds of distortion vary with the projection used. Some projections are suited for mapping large areas that are mainly north-south in extent, others for large areas that are mainly east-west in extent.

## Slide 41: Coordinate Systems
Hydrologic calculations are done in Cartesian or Planar coordinates (x,y,z)
Earth locations are measured in Geographic coordinates of latitude and longitude (f,l)
Map Projections transform (f,l) (x,y)

## Slide 42: Coordinate System
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin

## Slide 43: Commonly used coordinate systems and associated projections
State Plane (Texas, California, etc)
  Usually is a Lambert Conformal Conic projection (not always)
    Reference meridian
    Two standard parallels
    Good for East-West areas
    Commonly used by state and local governments for GIS databases
    Broken into appropriate sections representing areas of the state
  Coordinate System is in Feet
  False Easting (FE), False Northing (FN)
    Reference Latitude
    Central Meridian
    (0 + FE, 0 + FN) is origin of coordinate system

## Slide 44: Universal Transverse Mercator Coordinate System
Uses the Transverse Mercator projection
Each zone has a Central Meridian (lo), zones are 6° wide, and go from pole to pole
60 zones cover the earth from East to West
Reference Latitude (fo), is the equator
(Xshift, Yshift) = false easting and northing so you never have a negative coordinate
  This time in METERS!!!!!
Commonly used by federal govt
agencies such as USGS (also a few
states)

## Slide 45
Mercator
Projection
The only map on which a straight line drawn anywhere within its bounds shows a particular type of direction, but distances and areas are grossly distorted near the map's polar regions.

## Slide 46
UTM Projection (Zone 15)

## Slide 47: UTM Zone 14
Equator
-120°
-90 °
-60 °
-102°
-96°
-99°
Origin
6°

## Slide 48: Universal Transverse Mercator Projection

## Slide 49: Summary Concepts
Two basic locational systems: geometric or Cartesian (x, y, z) and geographic or gravitational (f, l, z)
Mean sea level surface or geoid is approximated by an ellipsoid to define a horizontal earth datum which gives (f, l) and a vertical datum which gives distance above the geoid (z)

## Slide 50: Summary Concepts (Cont.)
To prepare a map, the earth is first reduced to a globe and then projected onto a flat surface
Three basic types of map projections:
  conic
  cylindrical
  Planar/azimuthal
A particular projection is defined by a datum, a projection type and a set of projection parameters

## Slide 51: Summary Concepts (Cont.)
Standard coordinate systems use particular projections over zones of the earth’s surface
Types of standard coordinate systems:
  UTM
  State Plane
  Others too numerous to mention
Do not confuse the coordinate system of a set of datum for its projection
  Example: A shapefile that uses the Texas State Plane Coordinate System is in the Lambert Conformal Conic Projection

## Slide 52: Interrupted projections to maintain equal-area and be relatively conformal
Good for studying land areas, but not very good for ocean studies.

## Slide 53: What you get if you don’t interrupt
Areas may be equal (proper proportions); however, shapes are greatly distorted the farther one gets from the center of the projection

## Slide 54: Adapted to Keep Oceans together

## Slide 55: Unusual Special Purpose Projections

## Slide 56: Cylindrical equal-area projection with oblique orientation

## Slide 60: Peters is an equal-area projection which became the centerpiece of a controversy surrounding the political implications of map design

## Slide 61: The Hammer-Aitoff Projection

## Slide 63: This orientation is used in Australian geography textbooks (probably N.Z. too)

## Slide 65: This is only a sample – the variety is almost endless
The cartographer (map maker) will, one hopes, make choices carefully to truthfully communicate graphic information about the earth and parts. Unfortunately some people or groups want to push a particular agenda rather than truthfully inform people. Example: The Soviet Union was about 2.5 times larger than the U.S.A. (a fact). However, some overly militant Americans would show the countries on a Mercator projection and the Soviet Union would look 3.5 to 4 times bigger than the U.S. – their purpose was to scare people into supporting greater defense spending during the Cold War. See the next slide.

## Slide 66: Ro
Mercator Projection – conformal but distorts area, particularly at high latitudes.
Robinson equal-area projection keeps areas in correct proportion but distorts shape somewhat at high latitudes.

## Slide 67: What does all this mean???
Careful attention must be paid to the projection, datum and coordinate system for every piece of GIS data used.
Failure to use data from the same system OR change the data (re-project) it to the desired system will result in overlay errors
  Can range some small to SIGNIFICANT
  Real danger is when the errors are small (possibly unnoticed)
Shapefiles, images, grids all have this data inherent in their very creation.
  Usually included in a system of files known as “metadata” or xxxxxx.PRJ file.
Not only must a person select the projection which will most accurately convey the information to the viewer, but attention must also be paid to obtaining data from the same data system so that the computer will properly merge the layers
Gone are the days of the creatively hand-drawn maps of my youth. The thrill upon successful completion was fantastic, but GIS can be much more precise.

## Slide 68
Turned upside down yet??????
Excellent website: http://erg.usgs.gov/isb/pubs/MapProjections/projections.html